## Slide 1
h1
h2
s1
s2
s3
s5
s4
eth1
eth1
eth2
eth3
eth1
eth1
eth1
eth2
eth2
eth3
eth1
eth1
eth2
eth2
Our Topology

## Slide 2: Source Routing Forwarding
Our work (source routing):
OpenFlow 1.3
Repurpose vlan tag in 802.1Q headers to store path
Hosts know the whole path
Hosts build path in pkt headers
Switches forward pkts following path in their headers
Traditional forwarding:
Distributed routing decision
Switches forward pkts by looking up table (IP - port)

## Slide 3: Source Routing Header
Ethernet: dst=xx:xx:xx:xx:xx:xx src=xx:xx:xx:xx:xx:xx
802.1Q: vlan=out_port
...
802.1Q: vlan=out_port
IPV4: dst=dst_ip src=src_ip
ICMP: id=xxx seq=seq_num
Payload
ICMP packet headers
MAC address: not important
Multiple nested 802.1Q headers
Normal ICMP header structure

## Slide 4: Flow Entries
s1 flow table
..., table=0, n_packets=0, n_bytes=0, priority=2000,
dl_vlan=1 actions=pop_vlan,output:"s1-eth1“
..., table=0, n_packets=0, n_bytes=0, priority=2000,
dl_vlan=2 actions=pop_vlan,output:"s1-eth2“
..., table=0, n_packets=0, n_bytes=0, priority=2000,
dl_vlan=3 actions=pop_vlan,output:"s1-eth3"

## Slide 5: Example
h1 ping h2
Path: h1 - s1-s5-s4 - h2
Out ports: eth3-eth2-eth1 = [3, 2, 1]
Ethernet
802.1Q: vlan = 3
802.1Q: vlan = 2
802.1Q: vlan = 1
IPV4
ICMP
Payload
Ethernet
802.1Q: vlan = 2
802.1Q: vlan = 1
IPV4
ICMP
Payload
Ethernet
802.1Q: vlan = 1
IPV4
ICMP
Payload
Ethernet
IPV4
ICMP
Payload

## Slide 6: AI Utilization
Generate code template: Claude, Gemini
Code testing and debugging: Claude, Gemini
GUI Generation and Connection: Claude